## Slide 1: Cass River Water Quality Monitoring Project
Year Two Project Summary
Prepared by: Environmental Science Solutions, LLC
June 2014

## Slide 2: Project Background and Goals
The Cass River Greenway (CRG) organization contracted Environmental Science Solutions (ESS) to assist with fulfillment of its obligations pursuant to the Cass River Water Quality Monitoring Project grant (Project # 2011-0501) issued by the State of Michigan Department of Environmental Quality – Water Resources Division – Office of Surface Water Assessment.
The main goal of the project is to provide current baseline information to help determine watershed conditions along the main channel of the Cass River. Data and information from this project will be used to complement the current Cass River Watershed Management Plan and provide community members and stakeholders information about water quality within the study area.

## Slide 3: Project Study Area
The study area for the project is the main channel of the Cass River on the northern boundary of the Cass River Watershed from Cass City in the northeast to Bridgeport in the southwest in east central lower Michigan. Nine sampling sites are located near the municipalities of Cass City, Caro, Vassar, Frankenmuth and Bridgeport in Tuscola and Saginaw counties. (See site map on next slide).

## Slide 4: Project Study Area

## Slide 5: Sample Sites
Site Name | Site ID | Municipality | County | Latitude | Longitude | Watershed
Cemetery Rd. | CC2 | Cass City | Tuscola | 43.5847 | -83.1736 | Cass River
Dodge Rd. | CC1 | Cass City | Tuscola | 43.5698 | -83.2321 | Cass River
Dayton Rd. | C2 | Caro | Tuscola | 43.4901 | -83.3765 | Cass River
Wells Rd. | C1 | Caro | Tuscola | 43.4503 | -83.4401 | Cass River
Caine Rd. | V2 | Vassar | Tuscola | 43.3924 | -83.5222 | Cass River
Huron Rd. | V1 | Vassar | Tuscola | 43.3712 | -83.5803 | Cass River
Bray Rd. | F2 | Frankenmuth | Tuscola | 43.3244 | -83.6572 | Cass River
Beyer Rd. | F1 | Frankenmuth | Saginaw | 43.3287 | -83.7584 | Cass River
Fort Rd. | B1 | Bridgeport | Saginaw | 43.3486 | -83.8844 | Cass River

## Slide 6: Sample Parameters
Total Phosphorus
Total Suspended Solids
Fecal Coliform Bacteria
Nitrates
Turbidity
Temperature
pH
Dissolved Oxygen
Biological Oxygen Demand

## Slide 7: Year Two Sampling Summary Highlights
2013 Sampling season began about 3 weeks earlier than 2012 (Early- April vs. May)
2013 was a bit cooler and wetter sampling season. More significant rain events.
Variation from 2012 to 2013 includes:
Increased Phosphorus levels in the upper and lower reaches of the sampling area.
pH Values were lower throughout the sample area.
Nitrate Values were down throughout the sample area. Elevated values occurred throughout the sample area on the 4/24 sample date.
Total Suspended solids and Turbidity values were elevated in all but the Fort Rd. site (B1).
Biological Oxygen Demand values were increased at all sites

## Slide 8: Sample Results – Year Two
Site Name | Phosphorous | Total Suspended Solids | Fecal Coliform Bacteria | Nitrates | Turbidity | Temperature | pH | Dissolved Oxygen | Biochemical Oxygen Demand
Geometric Mean | mg/L | mg/L | Col / 100 ml | mg/L | NTU | ° F | Units | mg/L | mg/L
Cemetery Rd. (CC2) | 0.06 | 11.6 | 129 | 2.79 | 10.2 | 62.5 | 7.9 | 6.47 | 2.15
Dodge Rd. (CC1) | 0.05 | 9.0 | 175 | 2.55 | 9.1 | 62.6 | 7.9 | 6.57 | 2.44
Dayton Rd. (C2) | 0.007 | 14.5 | 94 | 2.63 | 14.9 | 63.5 | 8.0 | 6.23 | 2.38
Wells Rd. (C1) | 0.01 | 23.3 | 90 | 2.80 | 26.2 | 64.1 | 8.0 | 6.38 | 2.05
Caine Rd. (V2) | 0.05 | 13.6 | 55 | 2.71 | 13.9 | 63.2 | 8.0 | 6.49 | 2.16
Huron Rd. (V1) | 0.05 | 13.3 | 58 | 2.99 | 13.5 | 64.2 | 8.1 | 6.12 | 1.81
Bray Rd. (F2) | 0.10 | 13.9 | 189 | 2.10 | 10.2 | 64.3 | 8.1 | 6.24 | 1.96
Beyer Rd. (F1) | 0.10 | 20.2 | 163 | 2.11 | 13.5 | 64.6 | 8.0 | 6.20 | 2.03
Fort Rd. (B1) | 0.11 | 15.6 | 83 | 2.62 | 15.8 | 66.2 | 8.1 | 6.21 | 1.71
Study Area Geometric Mean | 0.04 | 14.46 | 105 | 2.57 | 13.50 | 63.90 | 8.00 | 6.32 | 2.06

## Slide 9: Annual Comparison

## Slide 10: Mean Value Comparison - Phosphorous
Chart: Phosphorous Mean Site Values (mg/L)
| Cemetery Rd. (CC2) | Dodge Rd. (CC1) | Dayton Rd. (C2) | Wells Rd. (C1) | Caine Rd. (V2) | Huron Rd. (V1) | Bray Rd. (F2) | Beyer Rd. (F1) | Fort Rd. (B1)
2012 Mean Value | 0.051988 | 0.036718 | 2.3403e-05 | 3.7924e-05 | 0.063466 | 0.055931 | 0.10185 | 0.085 | 0.091638
2013 Mean Value | 0.05626 | 0.045216 | 0.0068937 | 0.0072414 | 0.047693 | 0.048361 | 0.099665 | 0.10416 | 0.10852

## Slide 11: Mean Value Comparison - TSS
Chart: Total Suspended Solids Mean Site Values (mg/L)
| Cemetery Rd. (CC2) | Dodge Rd. (CC1) | Dayton Rd. (C2) | Wells Rd. (C1) | Caine Rd. (V2) | Huron Rd. (V1) | Bray Rd. (F2) | Beyer Rd. (F1) | Fort Rd. (B1)
2012 Mean Value | 6.1755 | 4.8618 | 13.0729 | 17.1497 | 11.8216 | 12.2898 | 10.713 | 13.0705 | 22.9866
2013 Mean Value | 11.5683 | 8.974 | 14.4503 | 23.2532 | 13.6459 | 13.257 | 13.8798 | 20.1755 | 15.6486

## Slide 12: Mean Value Comparison – Fecal Coliform
Chart: Fecal Coliform Bacteria (Colonies/ 100 ml)
| Cemetery Rd. (CC2) | Dodge Rd. (CC1) | Dayton Rd. (C2) | Wells Rd. (C1) | Caine Rd. (V2) | Huron Rd. (V1) | Bray Rd. (F2) | Beyer Rd. (F1) | Fort Rd. (B1)
2012 Mean Value | 95.5782 | 82.7239 | 40.6226 | 58.9495 | 56.5465 | 54.7807 | 134.1697 | 140.1402 | 130.064
2013 Mean Value | 129.2905 | 174.988 | 93.8519 | 90.1917 | 55.0488 | 57.9972 | 189.4553 | 162.8264 | 83

## Slide 13: Mean Value Comparison – Nitrates
Chart: Nitrates (mg/L)
| Cemetery Rd. (CC2) | Dodge Rd. (CC1) | Dayton Rd. (C2) | Wells Rd. (C1) | Caine Rd. (V2) | Huron Rd. (V1) | Bray Rd. (F2) | Beyer Rd. (F1) | Fort Rd. (B1)
2012 Mean Value | 3.032 | 3.2887 | 3.7006 | 3.9679 | 3.7537 | 3.8068 | 3.2937 | 3.5509 | 4.2265
2013 Mean Value | 2.7914 | 2.5457 | 2.6279 | 2.7981 | 2.7127 | 2.9933 | 2.0982 | 2.1087 | 2.621

## Slide 14: Mean Value Comparison – Turbidity
Chart: Turbidity (NTU's)
| Cemetery Rd. (CC2) | Dodge Rd. (CC1) | Dayton Rd. (C2) | Wells Rd. (C1) | Caine Rd. (V2) | Huron Rd. (V1) | Bray Rd. (F2) | Beyer Rd. (F1) | Fort Rd. (B1)
2012 Mean Value | 6.8587 | 4.6168 | 10.8621 | 14.1694 | 10.0791 | 11.6364 | 8.0951 | 9.5586 | 19.2374
2013 Mean Value | 10.2334 | 9.1059 | 14.8875 | 26.2068 | 13.9304 | 13.5044 | 10.2003 | 13.476 | 15.8189

## Slide 15: Mean Value Comparison – Temperature
Chart: Temperature (°F )
| Cemetery Rd. (CC2) | Dodge Rd. (CC1) | Dayton Rd. (C2) | Wells Rd. (C1) | Caine Rd. (V2) | Huron Rd. (V1) | Bray Rd. (F2) | Beyer Rd. (F1) | Fort Rd. (B1)
2012 Mean Value | 62.9467 | 62.9292 | 66.2933 | 65.7894 | 65.8617 | 66.2487 | 66.2237 | 67.8455 | 69.2038
2013 Mean Value | 62.4891 | 62.6008 | 63.4966 | 64.0675 | 63.1925 | 64.2152 | 64.3272 | 64.6386 | 66.1875

## Slide 16: Mean Value Comparison – pH
Chart: pH (pH Units)
| Cemetery Rd. (CC2) | Dodge Rd. (CC1) | Dayton Rd. (C2) | Wells Rd. (C1) | Caine Rd. (V2) | Huron Rd. (V1) | Bray Rd. (F2) | Beyer Rd. (F1) | Fort Rd. (B1)
2012 Mean Value | 8.1506 | 8.1867 | 8.3177 | 8.2476 | 8.2686 | 8.2866 | 8.2324 | 8.2341 | 8.284
2013 Mean Value | 7.8679 | 7.8606 | 8.0113 | 7.9812 | 7.9978 | 8.0927 | 8.088 | 8.0125 | 8.0614

## Slide 17: Mean Value Comparison – Dissolved Oxygen
Chart: Dissolved Oxygen (mg/L)
| Cemetery Rd. (CC2) | Dodge Rd. (CC1) | Dayton Rd. (C2) | Wells Rd. (C1) | Caine Rd. (V2) | Huron Rd. (V1) | Bray Rd. (F2) | Beyer Rd. (F1) | Fort Rd. (B1)
2012 Mean Value | 5.9789 | 6.1446 | 6.1467 | 5.8354 | 5.9024 | 5.8439 | 5.753 | 5.4736 | 5.9978
2013 Mean Value | 6.4719 | 6.5713 | 6.2307 | 6.3774 | 6.4877 | 6.1238 | 6.2368 | 6.2024 | 6.2053

## Slide 18: Mean Value Comparison– Biochemical Oxygen Demand
Chart: Biochemical Oxygen Demand (mg/L)
| Cemetery Rd. (CC2) | Dodge Rd. (CC1) | Dayton Rd. (C2) | Wells Rd. (C1) | Caine Rd. (V2) | Huron Rd. (V1) | Bray Rd. (F2) | Beyer Rd. (F1) | Fort Rd. (B1)
2012 Mean Value | 1.488 | 1.6268 | 1.5631 | 1.467 | 1.5069 | 1.3697 | 1.3637 | 1.2001 | 1.6078
2013 Mean Value | 2.1536 | 2.4365 | 2.3787 | 2.0512 | 2.1583 | 1.8084 | 1.9561 | 2.0302 | 1.7059

## Slide 19: Water Quality Index (WQI) Summary
Water Quality Index Range
WQI Value Rating
90 - 100 Excellent
70 - 90 Good
50 - 70 Medium
25 - 50 Poor
0 - 25 Very Poor

## Slide 20: Water Quality Index (WQI) Summary
Chart: Cass River Water Quality Index Values Cass City to Bridgeport
| Cemetery Rd. (CC2) | Dodge Rd. (CC1) | Dayton Rd. (C2) | Wells Rd. (C1) | Caine Rd. (V2) | Huron Rd. (V1) | Bray Rd. (F2) | Beyer Rd. (F1) | Fort Rd. (B1)
Mean Site WQI Value | 76.05 | 75.59 | 77.07 | 76.15 | 77.73 | 77.86 | 75.39 | 75.54 | 77.45
Mean WQI (Study Area) | 76.531 | 76.531 | 76.531 | 76.531 | 76.531 | 76.531 | 76.531 | 76.531 | 76.531

## Slide 21: Water Quality Index (WQI) Summary
Chart: WQI Annual Comparison 2012 and 2013 Sampling Seasons
| Cemetery Rd. (CC2) | Dodge Rd. (CC1) | Dayton Rd. (C2) | Wells Rd. (C1) | Caine Rd. (V2) | Huron Rd. (V1) | Bray Rd. (F2) | Beyer Rd. (F1) | Fort Rd. (B1)
2012 WQI Value | 75.95 | 76.77 | 78.03 | 77.13 | 76.26 | 76.07 | 75.44 | 73.9 | 75.96
2013 WQI Value | 76.05 | 75.59 | 77.07 | 76.15 | 77.73 | 77.86 | 75.39 | 75.54 | 77.45

## Slide 22: Water Quality Index (WQI) Summary
Site Name | 2012 Site WQI | 2013 Site WQI | Percent Change | 2013 WQI Rank | 2012 WQI Rank | Net Rank Change
Cemetery Rd. (CC2) | 76.0 | 76.1 | 0.13% | 6 | 7 | -1
Dodge Rd. (CC1) | 76.8 | 75.6 | -1.6% | 7 | 3 | -4
Dayton Rd. (C2) | 78.0 | 77.1 | -1.2% | 4 | 1 | -3
Wells Rd. (C1) | 77.1 | 76.2 | -1.3% | 5 | 2 | -3
Caine Rd. (V2) | 76.3 | 77.7 | 1.9% | 2 | 4 | 2
Huron Rd. (V1) | 76.1 | 77.9 | 2.3% | 1 | 5 | 4
Bray Rd. (F2) | 75.4 | 75.4 | -0.1% | 9 | 8 | -1
Beyer Rd. (F1) | 73.9 | 75.5 | 2.2% | 8 | 9 | 1
Fort Rd. (B1) | 76.0 | 77.5 | 1.9% | 3 | 6 | 3
Mean Value | 76.2 | 76.5 | 0.5% |  |  | 

## Slide 23: Water Quality Standard (WQS) Summary
Under weather conditions encountered, all sites met all statutory and generally accepted water quality standards. However, analysis indicated that heavy rain events and high temperatures can adversely affect bacteria levels.
All parameters for all sample all sites met state and EPA standards and scored in the good to excellent range in developed Water Quality Index standards.
Total suspended solids, nitrates, turbidity and Biochemical Oxygen Demand fall into the non-regulated category. Standards for these parameters are developed based on generally accepted water quality monitoring principles and practices.
Locally and Developed standards apply to E. Coli. This project measured fecal coliform. E. Coli is a subset of fecal coliform. Generally fecal coliform levels were below any thresholds that are a cause for public health concerns.

## Slide 24: Observations and Conclusions
The overall increase in solids, turbidity, phosphorous and fecal in year two is likely due to the timing and intensity of precipitation throughout the study area. Second year sampling saw more and heavier rainfall events during sampling days.
The decline in temperature in year two can largely be attributed to the earlier sampling season start date. Water temperature was significantly cooler during the April sampling events.
The decline in pH in year two can likely be attributed mainly to the earlier sampling season start date. Research shows that pH increases with water temperature. Additionally, early season runoff may contain snow melt which can be lower in pH than ambient river water. pH was lower throughout the watershed throughout the sampling season.
Increased DO and BOD levels in year two also follow from increased flow. Again, the timing and intensity of precipitation supports the increase in these parameters during year two.

## Slide 25: Recommendations
Extend sample season from early spring through late fall to capture seasonal variations in water chemistry.
Vary sample times within sample days to capture diurnal variation in sample parameters.
Conduct additional testing after rain events and during high temperatures to determine changes from steady state conditions
Investigate seasonal variation in pH – lower pH in early spring sample events.
Reducing flow rates from overland runoff during major rain events is key to slowing flow and reducing phosphorous and sediment loading levels.
Remain aware of DEQ’s potential action regarding tributary stream E. Coli standards (possible tributary studies including E. Coli and benthic monitoring) (Grant Opportunities).

## Slide 26: Project Partners
Cass River Greenway
Michigan Department of Environmental Quality
Cass City Municipal Wastewater Treatment Facility
Caro Municipal Wastewater Treatment Facility
Vassar Municipal Wastewater Treatment Facility
Frankenmuth Municipal Wastewater Treatment Facility
Saginaw Valley State University
Environmental Science Solutions, LLC

## Slide 27: References
Clair N. Sawyer, Perry L. McCarty, Gene F. Parkin (2003). Chemistry for Environmental Engineering and Science (5th ed.). New York: McGraw-Hill. ISBN 0-07-248066-1.
M. Mitchell, W. Stapp (2008). Field Manual (13th Edition) for Water Quality Monitoring. University of Michigan.
Correll, D.L (1998) Phosphorous: A rate Limiting Nutrient in Surface Waters. Edgewater Maryland Smithsonian Environmental Research Center.
Pfaffenberger, Roger C., Patterson, James H. 1977. Statistical Methods for Business and Economics. Irwin-Dorsey Limited, Georgetown, Ontario.
EPA 440/5-86-001, Quality Criteria for Water 1986.
Michigan Administrative Code, Part 4. Water Quality Standards. Rule 323.1041